## Slide 1
Dr. Cassie Jones
Assistant Professor of Feed Technology
Kansas State University
Manhattan, KS
jonesc@ksu.edu
WELCOME!
VM 101 | Rendered Ingredients

## Slide 2
By the end of the lesson, participants will be able to:
Identify rendered ingredients
List the component steps of the rendering process prior to receipt at the feed mill
Identify specialized equipment used to process rendered ingredients
List hazards associated with rendered ingredients
Lesson Objectives

## Slide 3
Utilizing otherwise unused foodstuffs & by-products
  48 billion lbs. annually
    5% restaurant grease
    4% grocery/butcher waste
    91% slaughter by-products
Average chemical composition of raw
  40 – 60% water
  20 – 30 % protein
  20 – 30% fat
Importance & Relevance
Slide # 3
Turning Waste Into Quality Ingredients
Notes: Photo of tissue and ingredients: NRA/Meeker

## Slide 4
Common Rendered Ingredients
Chart: 
| Ruminant meat and bone meal | Mixed ruminant/non-ruminant meat and bone meal | Poultry by-product meal | Non-ruminant mammalian meat and bone meal | Feather meal | Other proteins | Ruminant blood meal | Non-ruminant mammalian blood meal
Column1 | 30.9 | 15.2 | 18.9 | 17.1 | 7.3 | 5.3 | 2.6 | 2.5
Chart: 
| Inedible tallow | Edible tallow | Yellow grease | Choice white grease | Poultry fat | Edible lard | Other grease
Column1 | 36 | 21.5 | 18.8 | 11.1 | 10.1 | 1.3 | 1.2
Notes: Common Rendered Ingredients pie charts: C. Jones

## Slide 5
Feather Meal
Poultry Meal
Meat & Bone Meal
Blood Meal
Poultry Fat
Tallow
Choice White Grease
Yellow Grease
Spray-Dried Animal Plasma
Fish Meal
Common Rendered Ingredients
Notes: Photos of meals and grease: Iowa State University

## Slide 6
Quality Concerns
Slide # 6
Protein content of Meat and Bone Meal: Pearl, 2004
Chart: Individual Sample
Crude Protein | 57.2 | 47.5 | 59.08 | 55.21 | 55.06 | 55.76 | 46.29 | 55.26 | 47.13 | 53.02 | 57.05 | 57.17 | 57.04 | 48.02 | 55.04 | 45.88 | 53.39 | 48.9 | 47.15 | 47.9 | 56 | 52.24 | 56.14 | 51.32 | 55.89 | 47.48 | 55.43 | 49.58 | 58.52
Notes: Pearl, G. 2004. Tech Topics: Meat and bone meal usage in modern swine diets. Pages 50-53 in Render. The National Renderers Association, Camino, CA.

## Slide 7
Quality Concerns (cont.)
Moisture (%) | Pro-oxidant, diluent
Impurities | Pro-oxidant
Unsaponifiables | Sterols, pigments
Free Fatty Acids | Rancidity
Peroxide Value | Primary oxidation
Anisidine Value | Secondary oxidation
Iodine Value | Double bonds
Color | Processing damage
Active Oxygen Method | Retard oxidation

## Slide 8: Rendering Process
Wet Rendering Process
  Raw material exposed to hot water (180-205°F)
  Water later evaporated
  No longer used in U.S.
Notes: Graphic of rendering process: KSU

## Slide 9: Rendering Process (cont.)
Dry Rendering Process
  Raw material dehydrated in batch or continuous cookers at 240-290°F
  Total cooking time: 2-3 hours
  250°F and 2.8 bar, 45 minutes
  275°F and 2 bar, 30 minutes
  Water drained, solids pressed in screw press to extract fat

## Slide 10
Receiving and Sizing
  Goal: Receive products and sort into similar sizes
  Important for cooking
  Process: Sift and grind products
Rendering Process (cont.)
Sizing Process
Notes: Photo of sizing process: NRA/Meeker

## Slide 11
Heat Processing
  Goals:
    Destroy pathogens
    Melt fat to facilitate separation from bone and protein
    Remove water
Rendering Process (cont.)
Heat Processing
Notes: Photo of heat processing: NRA/Meeker

## Slide 12
Press
  Goal: Separate fat
  Process: Screw press in enclosed vessel separates fat from protein/bone
  Products: Fat to be refined to tallow or oil, protein to be refined to protein meals
Slide # 12
Press
Rendering Process (cont.)
Notes: Photo of press: NRA/Meeker

## Slide 13
Potential Hazards
  Physical: Glass, metal, wood
  Chemical: Cleaning substances
  Biological: Pathogens (bacteria, viruses)
Rendering Code of Practice (117 U.S. plants)
  Based on HACCP-like (Hazard Analysis Critical Control Point) principles
  Written procedures, process controls
  Third party auditing
  Preventative rather than responsive
Potential Feed Safety Hazards

## Slide 14
Potential Hazards (cont.)
Hazards Associated with Animal Carcass Disposal:
U.K. Department of Health, 2001
and Meeker, 2006
Potential Hazard to Humans | Rendering | Incineration | Landfill | Burial
E. coli | Very small | Very small | Moderate | High
Salmonella | Very small | Very small | Moderate | High
Listeria | Very small | Very small | Moderate | High
Camplylobactor | Very small | Very small | Moderate | High
Prions from BSE, scrapie | Moderate | Very small | Moderate | High
Notes: Meeker, D. L. 2009. North American Rendering – processing high quality protein and fats for feed. R. Bras. Zootec. 38:432-440.

## Slide 15
Pathogen | Raw tissues % samples positive | Post process 5 samples positive
Clostridium perfringens | 71.4 | 0
Listeria spp. | 76.2 | 0
L monocytogenes | 8.3 | 0
Campylocacter spp. | 29.8 | 0
C. Jejuni | 20.0 | 0
Salmonella spp. | 84.5 | 0
Efficacy of the U.S. rendering system in the destruction of pathogenic bacteria
Potential Hazards (cont.)
Notes: Troutt, H. F., D. Schaeffer, and I. Kakoma. 2001. Prevalence of selected foodborne pathogens in final rendered products. Fats and Proteins Research Foundation Directors Digest 132.

## Slide 16
Common rendered ingredients: feather meal, poultry meal, meat and bone meal, blood meal, spray dried animal plasma, fish meal, and respective fats
Processing steps include receiving and sizing, cooking, and pressing
Important equipment include sizing equipment, cookers, press, hammermills
Lesson Summary

## Slide 17
Potential feed safety hazards in rendered ingredients: physical, chemical and microbial hazards; hazard occurrence in rendered products minimized by correct implementation of Rendering Code of Practice.
Lesson Summary (cont.)

## Slide 18: This course was made possible by:
*Funding for this Grain and Feed Mill Operations course was made possible, in part, by the Food and Drug Administration through grant (1U54FD004333-01), views expressed in written materials or publications and by speakers and moderators do not necessarily reflect the official policies of the Department of Health and Human Services; nor does any mention of trade names, commercial practices, or organization imply endorsement by the United States Government.*