## Slide 1
WELCOME!
Dr. Cassie Jones
Assistant Professor of Feed Technology
Kansas State University
Manhattan, KS
jonesc@ksu.edu
VM 101 | Wheat Processing

## Slide 2
By the end of the lesson, participants will be able to:
Recognize components of wheat processing prior to receipt at feed mill
Identify classes of wheat and wheat by-products commonly used as animal feed ingredients
List food safety hazards associated with wheat and wheat by-products
Identify specialized equipment used to process wheat and wheat by-products
Lesson Objectives
Slide # 2

## Slide 3
Wheat is #3 field crop in U.S.
  Total acres have dropped 1/3 since 1981
Whole wheat (ground or steam-flaked)
  75% flour
  25% wheat by-products (midds, screenings)
Importance & Relevance
Slide # 3
Notes: Photo: USDA

## Slide 4
Six Wheat Classes
Slide # 4
Soft White
Soft Red Winter
Hard Red Winter
Hard White
Hard Red Spring
Durum
Notes: Photo: Chris Miller

## Slide 5
Six Wheat Classes cont.
Slide # 5
Notes: Graphic: U.S. Wheat Associates

## Slide 6
Process Flow
Slide # 6
Wheat from Field
Cleaning
Tempering
Grinding
Sifting
Purification
Flour
Screenings
Middlings
Germ
Red Dog

## Slide 7
Wheat Cleaning
Slide # 7
Wheat cleaned to remove:
  Non-Wheat Material
    Sticks, straw, stones, insects
  Wheat Not Fit for Milling
    Broken, damaged, small kernels
Notes: Photo: Chris Miller

## Slide 8
Wheat Cleaning, cont.
Slide # 8
Receiving Separator cleaning non-wheat material
Notes: Photo of Separator Machine: Chris Miller
Photo of Screen: Chris Miller
Photo of non-wheat: Chris Miller
Photo of small stones and non-wheat: Chris Miller
Photo of separator machine side view: Chris Miller
Photo of chaff: Chris Miller
Line drawing of separator machine:

## Slide 9
Wheat Cleaning, cont.
Slide # 9
Digital Optical Color Sorter
cleaning wheat not fit for milling
Notes: Photo of sorter machine: Chris Miller
Photo of dark wheat: Chris Miller
Photo of red wheat: Chris Miller

## Slide 10
Wheat Tempering
Slide # 10
Tempering System
Water/heat/steam applied to wheat and rested
  Soften endosperm
  “Toughen” bran
Wheat Foods Council
Bran
Endosperm
Germ
Notes: Photo of tempering machine: Chris Miller
Graphic of wheat kernel: Wheat Foods Council

## Slide 11
Wheat Grinding
Slide # 11
Rolls and Corrugations
Grinding actions
  Corrugations
  Pitch
  Spiral
Notes: Photo of roller mills: Chris Miller
Graphic of rolls: Chris Miller
Graphic of corrugations: Chris Miller

## Slide 12
Wheat Sifting
Slide # 12
Notes: Photo of sifter machine: Chris Miller
Graphic of particle separation: KSU

## Slide 13
Wheat Purification
Slide # 13
Particle Separation:
Mark Fowler, October 2012
Product Inlet
Air flow Out
Air flow IN
Before
After
Notes: Line drawing of purifier machine:
Line drawings of particle separation:

## Slide 14
Processing Prior to Feed Mill
Slide # 14
Wheat from Field
Cleaning
Tempering
Grinding
Sifting
Purification
Flour
Screenings
Middlings
Germ
Red Dog

## Slide 15
Wheat By-Products
Slide # 15
Cleaning
Tempering
Grinding
Sifting
Purification
Screenings
Middlings
Germ
Red Dog
Notes: Photos of wheat by-products: KSU

## Slide 16
Physical Hazards
  Non-grain material in screenings not caught by magnets
Chemical Hazards
  Chlorine used in tempering
  Pesticides/agrochemicals
Microbial Hazards
  Mold (Vomitoxin)
Potential Feed Safety Hazards
Slide # 16
Wheat Contaminated by Vomitoxin
Notes: Photo of wheat contaminated by Vomitoxin: USDA

## Slide 17
Prior to reaching the feed mill, wheat is processed by cleaning, tempering, grinding, sifting, and purification
The six classes of wheat are soft white, soft red winter, hard red winter, hard white, hard red spring, and durum
The most common wheat by-products are wheat screenings and wheat middlings
Potential feed safety hazards associated with wheat or wheat by-products include non-grain material, chlorine, pesticides or vomitoxin
Receiving separators, roller mills, sifters, and purifiers are important equipment
Lesson Summary
Slide # 17

## Slide 18: This course was made possible by:
*Funding for this Grain and Feed Mill Operations course was made possible, in part, by the Food and Drug Administration through grant (1U54FD004333-01), views expressed in written materials or publications and by speakers and moderators do not necessarily reflect the official policies of the Department of Health and Human Services; nor does any mention of trade names, commercial practices, or organization imply endorsement by the United States Government.*